## Slide 1: DIGITAL ELECTRONIC MINI PROJECT PRESENTATION
Four Way Traffic Light system
PRESENT BY GROUP:-M

## Slide 2: Group:-M Four Way Traffic Light system
RAHMAN KAZI ASHIKUR (B081910450)
MOHAMAD A’ARFAN BIN AZHAR (B081910059)
SUBJECT :-DIGITAL ELECTRONIC(BEEC2404)
LECTURER:NIZA MOHD IDRIS

## Slide 3: on 5 August 1914, the American Traffic Signal Company installed a traffic signal system
Figure.1:-Picture of Before traffic light system create
Group:-M Four Way Traffic Light system

## Slide 4: Four Way Traffic Light system Using D Flip Flop
Due to the increase in traffic, the user of vehicles is facing too many problems on roads. Sometimes the roads get block
Group:-M Four Way Traffic Light system

## Slide 5
PROBLEM STATEMENT
TO AVOID THE COLLISION OF VEHICLES
To control the consistency
of the cycle of the traffic.
To avoid collision vehicles with public
Group:-M Four Way Traffic Light system

## Slide 6: For this project we will discuss about.
Animation Video Of This Project
Block diagram of this project
Truth Table
Karnaugh Mapping (for Boolean expression )
Circuit design
PCP design
Group:-M Four Way Traffic Light system

## Slide 7: COMPONENTS OF THIS PROJECT.
D type flip flop (IC7474)
7 AND GATE(IC7408)
3 OR GATE(IC7432)
1 NOT GATE(IC7404)
BATTERY 9V
4 L.E.D traffic light
1 DIGITAL CLOCK GENERATOR
WIRE
Group:-M Four Way Traffic Light system

## Slide 8: ANIMATION VIDEO OF THIS PROJECT
Group:-M Four Way Traffic Light system

## Slide 9
2
NS=RE
EW=Y
1
NS=R
EW=G
5
NS=Y
EW=R
4
NS=G
EW=R
3
NS=R EW=R
6
NS=R
EW=R
Group:-M Four Way Traffic Light system
Diagram of this project
R1
A1
G1
R2
A2
G2

## Slide 10
N-S | E-W
RED | GREEN
RED | AMBER
RED | RED
GREEN | RED
AMBER | RED
RED | RED
RED | GREEN
State NO | R1 | A1 | G1 | R2 | A2 | G2
1 | 1 | 0 | 0 | 0 | 0 | 1
2 | 1 | 0 | 0 | 0 | 1 | 0
3 | 1 | 0 | 0 | 1 | 0 | 0
4 | 0 | 0 | 1 | 1 | 0 | 0
5 | 0 | 1 | 0 | 1 | 0 | 0
6 | 1 | 0 | 0 | 1 | 0 | 0
Group:-M Four Way Traffic Light system

## Slide 11: Select the type and number of flip-flops for the circuit
Since the number of states is equal to six, the minimum number of flip-flops, which can support six states.
The maximum number of flip-flops we have to use six (one flip-flop per state).
In our this design we will use three D-type flip-flops. There will be two unused states.
D1
D3
D2
Figured : D(data)FF
Group:-M Four Way Traffic Light system

## Slide 12
State | Q1 | Q2 | Q3 | R1 | A2 | G1 | R2 | A2 | G2
1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
2 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0
3 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0
4 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
5 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0
6 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0
7 | 0 | 0 | 0 | X | X | X | X | X | X
8 | 0 | 0 | 1 | X | X | X | X | X | X
We could, for example, make R1=Q1 and R2=Q2he third output, Q3 must be assigned such that all used states are distinct. One possible set of assignments are shown below:

## Slide 13
2
NS=RE
EW=Y
1
NS=R
EW=G
5
NS=Y
EW=R
4
NS=G
EW=R
3
NS=R EW=R
6
NS=R
EW=R
0,1
0
0
1
0
0,1
1
0

## Slide 14
R1
A1
G1
R2
A2
D1
D3
D2
G2
Group:-M Four Way Traffic Light system

## Slide 15: Title and Content Layout with Chart
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 4.3 | 2.5 | 3.5 | 4.5
Series 2 | 2.4 | 4.4 | 1.8 | 2.8
Series 3 | 2 | 2 | 3 | 5

## Slide 16: Two Content Layout with Table
First bullet point here
Second bullet point here
Third bullet point here
Class | Group 1 | Group 2
Class 1 | 82 | 95
Class 2 | 76 | 88
Class 3 | 84 | 90

## Slide 17: Title and Content Layout with SmartArt
Step 1 Title
Step 2 Title
Task description
Task description
Task description
Task description
Task description
Task description
Task description
Step 3 Title
Task description
Task description
Step 4 Title
Task description
Task description

## Slide 18: Add a Slide Title - 1

## Slide 19: Add a Slide Title - 2

## Slide 20: Add a Slide Title - 3

## Slide 22: Add a Slide Title - 4

## Slide 23: Add a Slide Title - 5